## Slide 1: Processor Datapath I
CS 3339
Lecture 7a
Greg LaKomski
Texas State University
Fall 2018
*some slides adopted from P&H

## Slide 2: Today We Begin – Processor Design !
THE PROCESSOR DATAPATH
  Implementation of instructions
    ALU
    Memory
    Branch – maybe today

## Slide 3: Processor Datapath and Control
At the micro-architectural level we have two types of components in the processor
  Datapath : set of components that combine to execute an instruction
    Bit of a misnomer – that’s an understatement. Lost in the annals of space and time.
  Control : set of components that tell the datapath what to do
    Works like an OS at the hardware level

## Slide 4: Processor Datapath and Control
Datapath and Control combine to provide a processor implementation
  elements are connected through wires
  only means of communication
  need to think in binary!
Each element in the datapath and the control unit has corresponding hardware
  We will not use an HDL in this class
    HDLs work best at a lower abstraction level
    Hardware Descriptive Language - Verilog
  We will use diagrams (like the one in the next slide) to understand the design and implementation issues

## Slide 5: Example Datapath Diagram

## Slide 6: Logic Design Basics
Information encoded in binary
  Low voltage = 0, High voltage = 1
  One wire per bit
  Multi-bit data encoded on multi-wire buses
Combinational and state elements
  ALU, MUX, Gates are combinational elements
    cannot store value
    output solely dependent on current input
  registers and memory are called state elements
    can store value

## Slide 7: Clock Cycle
We are assuming an edge triggered clocking methodology
Means values stored in a sequential logic element are updated on either a falling or rising edge.

## Slide 8: Sequential Logic
In digital circuit theory, sequential logic is a type of logic circuit whose output depends not only on the present value of its input signals but on the sequence of past inputs, the input history. ... Sequential logic is used to construct finite state machines, a basic building block in all digital circuitry.
wikipedia

## Slide 9: Sequential Logic

## Slide 10: Sequential Logic

## Slide 11: Datapath Elements : Gates
AND
OR
XOR
NOT

## Slide 12: Datapath Elements : Registers
Can store data
Implemented with D-flip-flops
  Delay the output
Set of registers implemented as a file
Special registers : PC
I0
D0
Q0
I1
D1
Q1
I2
D2
Q2
I3
D3
Q3
clk
4-bit register
PC

## Slide 13: REGISTER UNIT

## Slide 14: Datapath Elements : ALU
A
B
Y
+
A
B
Y
ALU
F
Adder
  Y = A + B
Arithmetic/Logic Unit
  Y = F(A, B)
Sometimes use specialized ALU (e.g. adders) if addition is all we need
Adders are ALUs hardwired to do addition

## Slide 15: ALU
OP1
OP2
RESULT
ALU
4 bit control
zero
overflow

## Slide 16: Datapath Elements : Multiplexer
C
s0
s1
D
M U X
Can’t just join wires together
Two wires in
Which one gets hooked to
D determined by C

## Slide 17: Datapath Elements : Memory
On chip memory
  aka the first level cache
Separate data and instruction memory
Slower than registers but faster than main memory
  2-10 cycles for loads
Larger than registers but smaller than main memory
read port
write port
address
on-chip
memory

## Slide 18: Memory Unit

## Slide 19: Processor Implementation
Implementing a processor implies implementing all instructions for a given ISA using the available datapath elements
Different instructions may have different resource requirements
Requirements for the same class of instructions will be similar
Some tasks we need to perform for every instruction
  Get the instruction (Fetch)
  Determine what instruction it is (Decode)

## Slide 20: Instruction Fetch
Need to
  Fetch an instruction
  Determine which instruction to fetch next
Components we need …
read port
write port
address
memory
PC
A
B
Y
ALU
F

## Slide 21: Instruction Fetch
Can send instruction address and compute next instruction in parallel
Specialized adder more efficient than regular ALU
Increment by 4 for next instruction
read
address
PC
ADD
4
instruction
read port
Instruction
Memory
(L1 I-Cache)
<
Notes: Block 1 for Edgar

## Slide 22: Instruction Execution
The tasks involved in instruction execution can be generalized as follows
  Fetch
  Decode
  Execute
    Depending on instruction class
      Use ALU to calculate
        Arithmetic result
        Memory address for load/store
        Branch target address
      Access data memory for load/store
  Fetch next …
Fetch-Decode-Execute Loop
A
A

## Slide 23: Question
How would the other instructions that affect the PC change this diagram???

## Slide 24: Instruction Fetch
Can send instruction address and compute next instruction in parallel
Specialized adder more efficient than regular ALU
Increment by 4 for next instruction
read
address
PC
ADD
4
instruction
read port
Instruction
Memory
(L1 I-Cache)
<
Maybe we have to get the PC+4 and add an offset plus shift left 2.
Notes: Block 1 for Edgar