## Slide 1
370726

## Slide 2: More Cache
CS 3339
Lecture 9b
Greg LaKomski
Texas State University
Fall 2018

## Slide 3: Announcements
Added updated instruction document to assignments

## Slide 4: More cache organizations
April 21, 2003
©2001-2003 Howard Huang
1
We want to store a copy of our most frequently used data in a small, fast cache memory, so we can speed up most data reads and writes.
  Normal programs exhibit temporal and spatial locality, which makes it easier to guess what data will be “most frequently used.”
  Last time we showed a basic direct-mapped cache, and discussed the need for additional tag and valid bits.
Today we’ll explore some more complex cache organizations.
  How can we take advantage of spatial locality too?
  How can we reduce the number of potential conflicts?

## Slide 5: Four important questions
When we copy a block of data from main memory to the cache, where exactly should we put it?
How can we tell if a word is already in the cache, or if it has to be fetched from main memory first?
Eventually, the small cache memory might fill up. To load a new block from main RAM, we’d have to replace one of the existing blocks in the cache... which one?
How can write operations be handled by the memory system?
Questions 1 and 2 are related—we have to know where the data is placed if we ever hope to find it again later!
5

## Slide 6: Tags
To find data stored in the cache, we need to add tags to distinguish between different memory locations that map to the same cache block.
Below, you can see that data from memory address 7 (0111) is stored in cache block 3, as opposed to data from addresses 3, 11 or 15.
Index 00
01
10
11
0000
0001
0010
0011
0100
0101
0110
0111
1000
1001
1010
1011
1100
1101
1110
1111
Tag
6
Data
00
11
01
01

## Slide 7: Spatial locality
What we can do is make the cache block size larger than one byte.
Here we use two- byte blocks, so we can load the cache with two bytes at a time.
If we read from address 12, the data in addresses 12 and 13 would both be copied to cache block 2.
One-byte cache blocks don’t take advantage of spatial locality, which predicts that an access to one address will be followed by an access to a nearby address.
Memory
Address 0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
0
1
2
3
Index
7

## Slide 8: Block addresses
Now how can we figure out where data should be placed in the cache?
It’s time for block addresses! If the cache block size is 2n bytes, we can conceptually split the main memory into 2n-byte chunks too.
To determine the block address of a byte address i, you can do the integer division
i ⁄ 2n
Our example has two-byte cache blocks, so we can think of a 16-byte main memory as an “8-block” main memory instead.
For instance, memory addresses 12 and 13 both correspond to block address 6, since 12 / 2 = 6 and 13 / 2 = 6.
Byte Address
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
1
8
2
3
4
5
6
7
Block Address
0

## Slide 9: Cache mapping
Once you know the block address, you can map it to the cache as before: find the remainder when the block address is divided by the number of cache blocks.
In our memory block 6 belongs in cache block 2, since
6 mod 4 = 2.
This corresponds to placing data from memory byte addresses 12 and 13 into cache block 2.
Byte Address
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
0
1
2
3
Index
1
9
2
3
4
5
6
7
Block Address
0

## Slide 10: Data placement within a block
When we access one byte of data in memory, we’ll copy its entire block
into the cache, to hopefully take advantage of spatial locality.
In our example, if a program reads from byte address 12 we’ll load all of memory block 6 (both addresses 12 and 13) into cache block 2.
Note byte address 13 corresponds to the same memory block address! So a read from address 13 will also cause memory block 6 (addresses 12 and
13) to be loaded into cache block 2.
To make things simpler, byte i of a memory block is always stored in byte
i of the corresponding cache block.
12
13
Byte Address
2
Cache Block
Byte 1
10
Byte 0

## Slide 11: Locating data in the cache
Let’s say we have a cache with 2k blocks, each containing 2n bytes.
We can determine where a byte of data belongs in this cache by looking at its address in main memory.
  k bits of the address will select one of the 2k cache blocks.
  The lowest n bits are now a block offset that decides which of the 2n bytes in the cache block will store the data.
Our example used a 22-block cache with 21 bytes per block. Thus, memory address 13 (1101) would be stored in byte 1 of cache block 2.
m-bit Address
(m-k-n) bits k bits
n-bit Block Offset
Tag | Index | 
4-bit Address
1 bit 2 bits
1-bit Block Offset
1 | 10 | 1
11

## Slide 12: A picture
1
Data
Index Valid Tag 0
1
2
3
Address (4 bits)
=
Hit
2
Block offset
Mux
Data
8
8
8
1
10
Tag
Index (2 bits)

## Slide 13: Using arithmetic
An equivalent way to find the right location within the cache is to use arithmetic again.
We can find the index in two steps, as outlined earlier.
  Do integer division of the address by 2n to find the block address.
  Then mod the block address with 2k to find the index.
The block offset is just the memory address mod 2n.
For example, we can find address 13 in a 4-block, 2-byte per block cache.
  The block address is 13 / 2 = 6, so the index is then 6 mod 4 = 2.
  The block offset would be 13 mod 2 = 1.
m-bit Address
(m-k-n) bits k bits
n-bit Block Offset
Tag | Index | 

## Slide 14: A diagram of a larger example cache
Here is a cache with 1,024 blocks of 4 bytes each, and
32-bit memory addresses.
Data
Index Valid Tag 0
1
2
3
...
... 1022
1023
=
Hit
Address (32 bits)
20 10
Tag
2 bits
Mux
Data
8
8
8
8
8

## Slide 15: A larger example cache mapping
Where would the byte from memory address 6146 be stored in this direct- mapped 210-block cache with 22-byte blocks?
We can determine this with the binary force.
— 6146 in binary is 00...01 1000 0000 00 10.
  The lowest 2 bits, 10, mean this is the second byte in its block.
  The next 10 bits, 1000000000, are the block number itself (512).
Equivalently, you could use your arithmetic mojo instead.
  The block offset is 6146 mod 4, which equals 2.
  The block address is 6146/4 = 1536, so the index is 1536 mod 1024, or 512.

## Slide 16: A larger diagram of a larger example cache mapping
Data
Index Valid Tag 0
1
2
... 512
... 1022
1023
Address (32 bits)
Hit
10
20
Tag
2 bits
Mux
8
Data
0000 .... 0001
 |  |  | 8 8 8 8 = |  |  |  | 
1000000000 10

## Slide 17: What goes in the rest of that cache block?
Data
Index Valid Tag
... 512
...
Hit
Tag
=
Mux
8
8
8
8
8
Data
The other three bytes of that cache block come from the same memory block, whose addresses must all have the same index (1000000000) and the same tag (00...01).
Address (32 bits)
0000 .... 0001 1000000000 10
20 10

## Slide 18: The rest of that cache block
Again, byte i of a memory block is stored into byte i of the corresponding cache block.
  In our example, memory block 1536 consists of byte addresses 6144 to 6147. So bytes 0-3 of the cache block would contain data from address 6144, 6145, 6146 and 6147 respectively.
  You can also look at the lowest 2 bits of the memory address to find the block offsets.
Block offset | Memory address | Decimal
00 | 00..01 1000000000 00 | 6144
01 | 00..01 1000000000 01 | 6145
10 | 00..01 1000000000 10 | 6146
11 | 00..01 1000000000 11 | 6147
... 512
...
Data
Index Valid Tag

## Slide 19: Disadvantage of direct mapping
However, this isn’t really flexible. If a program uses addresses 2, 6, 2, 6, 2, ..., then each access will result in a cache miss and a load into cache block 2.
This cache has four blocks, but direct mapping might not let us use all of them.
This can result in more misses than we might like.
00
01
10
11
Index
The direct-mapped cache is easy: indices and offsets can be decoded with bit operators or simple arithmetic, because each memory address belongs in exactly one block.
Memory
Address 0000
0001
0010
0011
0100
0101
0110
0111
1000
1001
1010
1011
1100
1101
1110
1111

## Slide 20: A fully associative cache
A fully associative cache permits data to be stored in any cache block, instead of forcing each memory address into one particular block.
  When data is fetched from memory, it can be placed in any unused block of the cache.
  This way we’ll never have a conflict between two or more memory addresses which map to a single cache block.
In the previous example, we might put memory address 2 in cache block 2, and address 6 in block 3. Then subsequent repeated accesses to 2 and 6 would all be hits instead of misses.
If all the blocks are already in use, it’s usually best to replace the least recently used one, assuming that if it hasn’t used it in a while, it won’t be needed again anytime soon.

## Slide 21: The price of full associativity
However, a fully associative cache is expensive to implement.
  Because there is no index field in the address anymore, the entire
address must be used as the tag, increasing the total cache size.
  Data could be anywhere in the cache, so we must check the tag of
every cache block. That’s a lot of comparators!
Index Valid Tag (32 bits) Data
...
...
...
Address (32 bits)
=
Hit
32
Tag
=
=

## Slide 22: Set associativity
An intermediate possibility is a set-associative cache.
  The cache is divided into groups of blocks, called sets.
  Each memory address maps to exactly one set in the cache, but data may be placed in any block within that set.
If each set has 2x blocks, the cache is an 2x-way associative cache.
Here are several possible organizations of an eight-block cache.
Set 0
1
2
3
4
5
6
7
0
1
2
3
Set
0
1
Set
1-way associativity 8 sets, 1 block each
2-way associativity 4 sets, 2 blocks each
4-way associativity 2 sets, 4 blocks each

## Slide 23: Locating a set associative block
Our arithmetic computations now compute a set index, to select a set
within the cache instead of an individual block.
Block Offset = Memory Address mod 2n Block Address = Memory Address / 2n
Set Index
= Block Address mod 2s
Address (m bits)
We can determine where a memory address belongs in an associative cache in a similar way as before.
If a cache has 2s sets and each block has 2n bytes, the memory address can be partitioned as follows.
(m-s-n) s n
Tag | Index | 
Block offset

## Slide 24: Example placement in set-associative caches
Where would data from memory byte address 6195 be placed, assuming the eight-block cache designs below, with 16 bytes per block?
• 6195 in binary is 00...0110000 011 0011.
Each block has 16 bytes, so the lowest 4 bits are the block offset.
For the 1-way cache, the next three bits (011) are the set index. For the 2-way cache, the next two bits (11) are the set index. For the 4-way cache, the next one bit (1) is the set index.
The data may go in any block, shown in green, within the correct set.
0
1
2
3
4
5
6
7
0
1
2
3
0
1
1-way associativity 8 sets, 1 block each
Set
2-way associativity 4 sets, 2 blocks each
Set
4-way associativity 2 sets, 4 blocks each
Set

## Slide 25: Block replacement
Any empty block in the correct set may be used for storing data.
If there are no empty blocks, the cache controller will attempt to replace the least recently used block, just like before.
It’s difficult to keep track of what’s really the least recently used block, so some approximations are used. We won’t get into the details.
0
1
2
3
4
5
6
7
0
1
2
3
0
1
1-way associativity 8 sets, 1 block each
Set
2-way associativity 4 sets, 2 blocks each
Set
4-way associativity 2 sets, 4 blocks each
Set

## Slide 26: Set associative caches are a general idea
By now you may have noticed the 1-way set associative cache is the same as a direct-mapped cache.
Similarly, if a cache has 2k blocks, a 2k-way set associative cache would be the same as a fully-associative cache.
0
1
2
3
4
5
6
7
0
1
2
3
Set
0
1
Set
1-way 8 sets,
1 block each
Set
2-way 4 sets,
2 blocks each
4-way 2 sets,
4 blocks each
0
Set
8-way 1 set,
8 blocks
direct mapped
fully associative

## Slide 27: 2-way set associative cache implementation
0
...
2k
Tag
Data
Index Valid
=
Hit
k
(m-k-n)
2-to-1 mux
2n
Valid Tag
Data
2n
2n Data
=
Address (m bits) Tag Index
Block offset
How does an implementation of a 2-way cache compare with that of
a fully-associative cache?
Only two comparators are
needed.
The cache tags are a little shorter too.

## Slide 28: Summary
Larger block sizes can take advantage of spatial locality by loading data from not just one address, but also nearby addresses, into the cache.
Associative caches assign each memory address to a particular set within the cache, but not to any specific block within that set.
  Set sizes range from 1 (direct-mapped) to 2k (fully associative).
  Larger sets and higher associativity lead to fewer cache conflicts and lower miss rates, but they also increase the hardware cost.
  In practice, 2-way through 16-way set-associative caches strike a good balance between lower miss rates and higher costs.